## Slide 1
ESP32 Wi‑Fi Scanner
Passive network discovery (SSID • RSSI • Channel • Encryption)
Goal
Show how an ESP32 can scan for nearby Wi‑Fi networks and print metadata to the Serial Monitor — without connecting to any network.
Outputs
• SSID (name)
• RSSI (signal strength)
• Channel
• Encryption/auth mode
• BSSID (AP MAC)
Ethics
Scanning is for learning/measurement in authorized environments. This demo does not capture traffic or passwords.
Notes: [Sources] - https://docs.espressif.com/projects/arduino-esp32/en/latest/api/wifi.html (WiFi.scanNetworks, WiFi.mode, WiFi.scanDelete) - https://github.com/espressif/arduino-esp32/blob/master/libraries/WiFi/examples/WiFiScan/WiFiScan.ino (reference scan example) [/Sources]

## Slide 2
Setup (Arduino IDE + ESP32 board)
What you need to upload and run the scanner
Software steps
1. Install Arduino IDE 2.x
2. Boards Manager → install “esp32 by Espressif Systems”
3. Tools → Board → select your ESP32 (ex: AI Thinker ESP32‑CAM)
4. Tools → Port → select your COM port
5. Upload the sketch
6. Tools → Serial Monitor @ 115200 baud
Hardware notes
• Any ESP32 dev board works
• ESP32‑CAM often needs a USB‑to‑Serial adapter
• Some boards require holding BOOT during upload
Tip: Serial baud must match
Code: Serial.begin(115200);
Serial Monitor: set 115200
Notes: [Sources] - https://docs.espressif.com/projects/arduino-esp32/en/latest/api/wifi.html (ESP32 Arduino Wi‑Fi API) - https://www.arduino.cc/en/Tutorial/ScanNetworks (Arduino scan networks concept example) [/Sources]

## Slide 3
How it works
High-level flow of the scanner sketch
setup():
Serial.begin(115200)
→
WiFi.mode(WIFI_STA)
WiFi.disconnect()
→
loop():
WiFi.scanNetworks()
→
Print each network:
SSID / RSSI / ENC
Key idea
The ESP32 can discover nearby access points by scanning. The scan returns a list of networks, and you can read properties like SSID and RSSI for each entry.
We convert the encryption/auth enum into readable labels (OPEN, WPA2, WPA3…) for the demo.
Important calls
WiFi.scanNetworks()
WiFi.SSID(i)
WiFi.RSSI(i)
WiFi.channel(i)
WiFi.encryptionType(i)
WiFi.scanDelete()
Notes: [Sources] - https://docs.espressif.com/projects/arduino-esp32/en/latest/api/wifi.html (WiFi.scanNetworks signature and WiFi.scanDelete) - https://github.com/espressif/arduino-esp32/blob/master/libraries/WiFi/examples/WiFiScan/WiFiScan.ino (example usage patterns) [/Sources]

## Slide 4
Demo output
How to read SSID, RSSI, channel, and encryption
Serial Monitor (example)
Networks found: 3
1) SSID: MyWiFi | RSSI: -52 dBm (4/4) | CH: 6 | ENC: WPA2 | BSSID: AA:BB:CC:DD:EE:FF
2) SSID: <hidden> | RSSI: -71 dBm (2/4) | CH: 11 | ENC: WPA2/WPA3 | BSSID: 11:22:33:44:55:66
3) SSID: Guest | RSSI: -86 dBm (1/4) | CH: 1 | ENC: OPEN | BSSID: 77:88:99:AA:BB:CC
--------------------------------------------------
How to interpret
• RSSI is signal strength in dBm (closer to 0 = stronger).
• Channel helps detect congestion/interference.
• Encryption shows the auth mode (OPEN/WPA2/WPA3…).
• Hidden SSID means the name isn’t broadcast.
Notes: [Sources] - https://docs.espressif.com/projects/arduino-esp32/en/latest/api/wifi.html (scan result fields and helpers) - https://randomnerdtutorials.com/esp32-useful-wi-fi-functions-arduino/ (example use of RSSI, SSID, scan) [/Sources]

## Slide 5
Troubleshooting & takeaways
Common issues + what I learned
Troubleshooting (what I hit)
• Compile error: `Serial.prinln` → typo (should be `Serial.println`)
• Gibberish output → Serial Monitor baud mismatch (set 115200)
• Upload trouble (ESP32‑CAM) → hold BOOT during upload, check board/port
• Some SSIDs appear “hidden” → normal; name not broadcast
Ethics / scope
This demo is scan‑only (no connection, no packet capture). Use only in authorized spaces and avoid sharing identifying network details publicly.
Future improvements
• Sort by strongest signal
• Log scans to CSV
• Visualize channels (2.4 GHz overlap)
• Add timestamping
Notes: [Sources] - https://docs.espressif.com/projects/arduino-esp32/en/latest/api/wifi.html (scanDelete and scanning behavior) [/Sources]